## Slide 1: CCSB Loads Water Years 2010-17
C. Alpers and S. Rose
USGS CAWSC
Dec. 11, 2018

## Slide 6: Difference in trap efficiency between THg and bulk sediment
In LOADEST models, Lower trap efficiency of pTHg (~62%) vs. sediment (~70%)
  Caused by higher [THg] on particles that exit basin compared with those that enter basin and those that are trapped
    Ratio of pTHg load to SS load, Inflow: 229 ng/g
    Ratio of pTHg load to SS load, Outflows: 295 ng/g
    Calculated pTHg, trapped sediment: 201 ng/g
Most likely explanation is grain-size effect
  Finer particles that exit basin have higher pTHg than bulk sediment entering basin
  Relatively coarse particles (sand and coarse silt) that are preferentially trapped in basin are lower in pTHg than inflow or outflow

## Slide 7
In:
65 kg/yr pTHg
282 x 106 kg/yr sediment
229 ng/g
Trapping of Particulate Total Mercury (pTHg) and Sediment in CCSB
Water Years 2010–17
Out:
25 kg/yr pTHg
84 x 106 kg/yr sediment
295 ng/g
Trapped:
40 kg/yr pTHg
198 x 106 kg/yr sediment
201 ng/g
Trap Efficiency:
62% pTHg
70% sediment
Results from LOADEST model, run in 2 batches: WY 2010-15, and WY 2016-17